## Slide 1: Q1: Internal Comparison
 | WETbLab 1 | WETbLab 2 | Percent difference
Condition | F Counts (695 nm) | F Counts (695 nm) | (%)
air_lights_on | 44 | 90 | 17.16
air_lights_off | 54 | 60 | 2.63
tape_air | 51 | 49 | 1.00
tape_DIW | 46 | 29 | 11.33
no_tape_DIW | 48 | 48 | 0.00
no_tape_tap | 50 | 50 | 0.00
no_tape_FilteredDRE | 68 | 65 | 1.13
 | Turner 1 | Turner 2 | Percent difference
Condition | (mv) | (mv) | (%)
air_lights_on | 0 | 0 | 0
air_lights_off | 0 | 0 | 0
DI water | 0 | 0 | 0
Tap water | 0 | 0 | 0
Filtered DRE water | 85 | 85 | 0
Meters generally agree between groups (some slightly off)
Variations could be due to meter position, taping method, etc
No tape for the appropriate blank (DI or SW) appears the most consistent (keep in mind only 2 points)

## Slide 2: Q1: T and P Effect Tests
Temperature Test
Remove bubbles
Fix sensor, larger bucket
Put bucket in makeshift recirculating bath
Increase temperature gradually, keeping internal T well-mixed
Make F measurements to see if there are changes
Pressure Test
Remove bubbles
Fix sensor in x-y, deep tank
Increase P by incrementally lowering the sensor and allowing for equilibration
Make F measurements to see if there are changes
Notes: If the tank is very large you might need to take into account temperature changes, could monitor temperature

## Slide 3: Q2: Wall and Movement Effects
Tested putting the meter near the walls, no apparent change (variability in numbers already high)
If we could detect changes we’d expect…the wall would add to the reflectance
  Regular water = higher values near the side
  Chlorophyll water = lower values near the side
Moving sensor: effect would depend on how homogenous/mixed the sample is and if your arm can move at speeds close to light
Notes: Ishan tested this and said no change