## Slide 1: Group 1: Ed PAR Values
 | PAR (W/m2) | 
 | Lee Method | Immersion Method
Away from Sun | 338.7 | 328.6
Into Sun | 371.3 | 340.0
Into Sun with Waves | 369.7 | ---
Values should be all approximately the same, as orientation of the HyperPro should have minimal effect on the Ed sensor
A drop was observed between Group 1 and Group 2, but it was likely just a function of time of day (next slide)
If the point was to find ways to occlude the Ed sensor, we did not achieve that.

## Slide 2: Group 2: Ed PAR Values
 | PAR (W/m2) |  |  |  | 
 | Lee Method |  | Immersion Method |  | 
 | Trial #1 | Trial #2 | Trial #1 | Trial #2 | Trial #3
Rotated | 223.0 | - | 294.5 | 297.9 | -
Off dock | 198.8 | 207.0 | - | - | -
Upriver | 242.7 | - | 292.4 | 202.2 | -
Downriver | 213.6 | - | 199.4 | - | -
Into sun | 223.1 | - | 325.3 | 309.5 | 308.0

## Slide 3: Kd from Secchi Disks
From ACS data, a(530nm)=0.54, c(530nm)=2.51
Poole & Atkins (1929) calculated that zsc agrees well with 1.7/Kd
  for our case, Z_sc=2.13m, K_d=0.8
Idso & Gilbert (1974) did a number of experiments using (then) modern equipment which found that Poole & Atkins was surprisingly accurate.
Other relationships have been suggested, but Poole & Atkins appears to have a solid body of evidence in a number of different waters.
Notes: It’s possible changes in light during the day will change k_d