## Slide 1: Sky radiance distribution
Figure give a example of simulated sky radiance distribution with solar zenith angle at 300, in the azimuth planes 00-1800.
The radiance peak occurs in the solar zenith angle and radiance decreased at both directions away the sun.
(Liang and Lewis, 1996)

## Slide 2: Ocean Optic Spectrometer
Detector range: 200-1100 nm
Integration time: 3.8 ms - 10 seconds
Dark noise: 50 RMS counts

## Slide 3: Spec Calibration
E: Irradiance
L: Radiance
M: Measurement
D: Dark
B: Bulb measurement
T: Integration time
We normalized measurements by integration time.

## Slide 4: Practical Aspects
Difficult to get full coverage quickly.
Very sensitive to noise.
Must normalize to integration time.
Need horizon views.
Must fully understand azimuth and zenith angle definitions
Arm gets tired

## Slide 5: Calibration results
Radiance = Irradiance *R/PI

## Slide 6: Group 1: Ed PAR Values
 | PAR (W/m2) | 
 | Lee Method | Immersion Method
Away from Sun | 338.7 | 328.6
Into Sun | 371.3 | 340.0
Into Sun with Waves | 369.7 | ---
Values should be all approximately the same, as orientation of the HyperPro should have minimal effect on the Ed sensor
A drop was observed between Group 1 and Group 2, but it was likely just a function of time of day (next slide)
If the point was to find ways to occlude the Ed sensor, we did not achieve that.

## Slide 7: Group 2: Ed PAR Values
 | PAR (W/m2) |  |  |  | 
 | Lee Method |  | Immersion Method |  | 
 | Trial #1 | Trial #2 | Trial #1 | Trial #2 | Trial #3
Rotated | 223.0 | - | 294.5 | 297.9 | -
Off dock | 198.8 | 207.0 | - | - | -
Upriver | 242.7 | - | 292.4 | 202.2 | -
Downriver | 213.6 | - | 199.4 | - | -
Into sun | 223.1 | - | 325.3 | 309.5 | 308.0

## Slide 8: Secchi Disks
Invented in 1865 by Pietro Angelo Secchi
One of the few human-eye measurements still made today.
Surprisingly consistent among operators
AOP related to Kd and c

## Slide 9: Kd from Secchi Disks
From ACS data, a(530nm)=0.54, c(530nm)=2.51
Poole & Atkins (1929) calculated that zsc agrees well with 1.7/Kd
  for our case, Z_sc=2.13m, K_d=0.8
Idso & Gilbert (1974) did a number of experiments using (then) modern equipment which found that Poole & Atkins was surprisingly accurate.
Other relationships have been suggested, but Poole & Atkins appears to have a solid body of evidence in a number of different waters.
Notes: It’s possible changes in light during the day will change k_d

## Slide 10
Ed looks like we expected. Rotation didn’t affect it.
Lu doesn’t look so great, may have forgotten to turn off “immersion” setting?

## Slide 11
Ed, when rotated into the sun, was lower for two separate trials. Would have expected them to be more similar, like last plot. Cloud, perhaps?
Lu has replicates that look good, and all look as we’d expect:
  All spectra suggest green waters, which is definitely what we see from the dock
  Lu was lower when Ed detector was rotated into the sun (Lu detector was in instrument’s shadow)

## Slide 12: Remote Sensing Reflectance (Rrs)
Rrs higher towards sun than away from sun.
Both Lee and Immersed Lu are comparable to the WISP and HyperSass data.
Rrs will improve with better K measurement.
Notes: Solid lines are the ones where Lu radiometer is facing the sun and the dashed are the ones where it is not facing the sun.
Blue are the Lee methods
Red are the Immersed Lu data
Green lines border both- upper is the c and lower is the a

## Slide 13: HyperSAS
Measures Lt (Lw + reflected Ls) and Ls in a single discreet direction
  Direction and angle between Lt and Ls measurements can be varied
Also measures Ed
RRS can be calculated as RRS=(Lt-ρLs)/Ed where ρ can be estimated.
  ρ estimated as 0.28 in this case

## Slide 14: Rrs Sensitivity to Azimuth Angle
Rrs measured at the theoretical optimum angle of 35˚, 135˚ falls in between measurements made at other zenith angles

## Slide 15
Rrs Sensitivity to Zenith Angle
Measurements at multiple zenith angles was limited (only two at the same azimuth angle).
Zenith appears to cause a much larger difference at 45˚ degree azimuth then at a 90 ˚ azimuth

## Slide 16: Seaweed in HyperSAS
Group 2 pulled seaweed in front of the HyperSAS to determine its effect on the measurement.
  Intentional contamination showed a clear “red edge” reflectance
Group 1 thought it may have had seaweed contamination on one reading.
  Little effect from accidental contamination in this case

## Slide 17: WISP (Water Insight SPectrometer)
Hand-held hyperspectral spectrometer
Provides Ro (reflectance), Lu, Ld, Ed
One vertical (up) spectrometer, 2 spectrometers at 42 degrees
Measures 400 – 800 nm

## Slide 18: WISP
Issues:
Group 2: Not functioning
Group 1: Lacking proper notes for all samples
Future Suggestions:
Syncronize watch with meter time
Always right down Chl and TMS readings when measuring for later file matching
Meter setting for Rrs export?
Notes: I took notes with some times, angles, and chl values but that was not enough to match all of the data, we had about 20 results and could only match 6 of them based on spectra, some of them we could guess at by what the shape/reflectance values looked like but not enough to say anything about definitive angle

## Slide 19: WISP Data*
Upper Dock
135E Kelp
Dock shows high reflectance, location with kelp shows high reflectance in the 700-800 range, all other samples (including 135E no kelp) show similar trends
1/sr
Sample | Chl (ug/L)
UD-60W | 0.2
Dock | 0
LD-30E | 0.1
LD-135E | 1.3
LD-135E Kelp | 167.5
LD-180 | 0.6
Notes: Only WISP data that we could make sure of the angles and measurements is on this graph, you can see the dock is super high, the kelp deviates from all the other samples

## Slide 20
Lower Reflectance Data
UD = upper dock, Ld = lower dock
All angles are from 0 degrees = sun
135E Kelp
1/sr
Sample | Chl (ug/L)
UD-60W | 0.2
Dock | 0
LD-30E | 0.1
LD-135E | 1.3
LD-135E Kelp | 167.5
LD-180 | 0.6
Notes: This shows the bottom half of the last graph in more detail, you can see the variation in the kelp sample versus the rest (interesting shape in the higher wavelengths), most other chlorophyll values are much lower

## Slide 21: Lower Dock Only
ReflectanceIncreases
Angle Increases
Sample | Chl (ug/L)
LD-30E | 0.1
LD-135E | 1.3
LD-180 | 0.6
Notes: Highest reflectance is at 30

## Slide 22
From Rrs to Rw
Notes: solid lines are calculated from Lu Ld Ed given by instrument; dotted lines are Ro value that the machine gives
You have to convert the values given to get at Rrs, there’s some weird conversion. Maybe we can set up the meter to do this for us???

## Slide 23: From Rrs to Rw

## Slide 24: HyperSAS and WISP Comparison
WISP compares well to HyperSAS data for common zenith and azimuth angles
WISP underestimates Rrs for long wavelengths in both cases
35˚, 135˚
35˚, 180˚