## Slide 1: HyperSAS
Measures Lt (Lw + reflected Ls) and Ls in a single discreet direction
  Direction and angle between Lt and Ls measurements can be varied
Also measures Ed
RRS can be calculated as RRS=(Lt-ρLs)/Ed where ρ can be estimated.
  ρ estimated as 0.28 in this case

## Slide 2: Seaweed in HyperSAS
Group 2 pulled seaweed in front of the HyperSAS to determine its effect on the measurement.
  Intentional contamination showed a clear “red edge” reflectance
Group 1 thought it may have had seaweed contamination on one reading.
  Little effect from accidental contamination in this case